## Slide 1
TUGAS AKHIR
RoRo
Smart Robot Rollator
Tongkat Jalan Pintar Berbasis ESP32 dengan Kendali Motor, Deteksi IMU, SOS & Monitoring Realtime
Tim Pengembang | 2025
Platform: ESP32 • Framework: Arduino / PlatformIO Bahasa: C++ • Real-time FreeRTOS • Cloud: Firebase + HiveMQ
ESP32
IMU
MQTT
Firebase
Firmware ESP32

## Slide 2
01
Latar Belakang
Mengapa RoRo dibangun?
RoRo — Smart Rollator | Firmware ESP32
2 / 10
Populasi Lansia Meningkat
Jumlah lanjut usia di Indonesia terus bertambah. Risiko jatuh tinggi — butuh alat bantu yang lebih cerdas.
Rollator Konvensional Pasif
Tongkat jalan tradisional tidak memberi umpan balik. Tidak ada monitoring kondisi pengguna secara realtime.
Keselamatan & Respons Darurat
Tidak ada mekanisme SOS otomatis. Keluarga / perawat tidak bisa memantau jarak jauh.
✔ Solusi: RoRo — Smart Rollator
Rollator bermotor dengan kendali kecepatan adaptif • Deteksi gerakan IMU (berjalan vs diam) • Tombol SOS + notifikasi realtime Dashboard lokal via HTTP • History tersimpan di Firebase Firestore • Push instan ke Flutter app via MQTT HiveMQ

## Slide 3
02
Arsitektur Sistem
Dua domain eksekusi — realtime & networking terpisah
RoRo — Smart Rollator | Firmware ESP32
3 / 10
Core 1 — FreeRTOS Tasks (Realtime)
TaskSafety
Prio 3 • 20 ms
SOS button, buzzer state machine, speed beep
TaskMotor
Prio 2 • 10 ms
BTS7960 PWM, potentiometer, gas button + latch
TaskIMU
Prio 2 • 120 ms
MPU6050 I2C, motionScore EMA, deteksi berjalan/diam
Queue*() non-blocking
➡
Arduino loop() — Networking (Best-Effort)
wifiManagerLoop
WiFi AP/STA state machine, mDNS rorro.local
firebaseManagerLoop
Firestore REST HTTPS — history & storage
mqttManagerLoop
HiveMQ TLS 8883 — push realtime ke Flutter
webServerLoop
HTTP API port 80 + dashboard.html
Shared State: RobotData struct • portMUX_TYPE critical sections • volatile gActiveMotorSpeed / gSpeedLevelChanged

## Slide 4
03
Fitur Utama
Lima modul firmware RoRo
RoRo — Smart Rollator | Firmware ESP32
4 / 10
Kendali Motor DC
▶ BTS7960 H-bridge x2 (kiri & kanan)
▶ PWM 5 kHz, 8-bit, 0-250 level
▶ 9 level kecepatan via potensiometer
▶ Tombol gas + latch triple-tap (3x ketuk = terkunci)
▶ Konfirmasi beep saat ganti level kecepatan
Deteksi Gerak IMU
▶ MPU6050 6-axis I2C (GPIO 21/22)
▶ motionScore = accelDelta × 3.5 + gyroMag / 45
▶ EMA smoothing α=0.25 @ 120 ms
▶ Histerisis: ON ≥0.32, OFF ≤0.18
▶ Status: berjalan / diam
SOS & Keselamatan
▶ Tombol SOS GPIO 4 (active-LOW)
▶ Buzzer GPIO 5 (toggle 250 ms) saat SOS
▶ Notifikasi Firebase + MQTT instan
▶ TaskSafety prioritas tertinggi (prio 3)
▶ Motor stop sebelum aksi jaringan
Dashboard Lokal & API
▶ HTTP API port 80 (GET/POST)
▶ GET /api/status — full state JSON
▶ POST /api/motor/test — uji motor manual
▶ POST /api/sos/test — simulasi SOS
▶ dashboard.html polling tiap 1 detik
Cloud & Realtime Push
▶ Firebase Firestore — history & storage
▶ MQTT HiveMQ TLS 8883 — live push
▶ Deferred-queue: tasks tidak blocking
▶ Retained message: subscriber langsung dapat state
▶ Last Will: status offline otomatis

## Slide 5
04
Tech Stack
Hardware, firmware, cloud, dan mobile
RoRo — Smart Rollator | Firmware ESP32
5 / 10
Hardware
• ESP32 DevKit (Xtensa LX6, 240 MHz, dual-core)
• MPU6050 — Accelerometer + Gyroscope 6-axis
• BTS7960 H-Bridge Driver x2 (motor kiri & kanan)
• DC Motor x2 (rollator kiri & kanan)
• Potensiometer 10K (GPIO 34, ADC 12-bit)
• Buzzer aktif-LOW (GPIO 5)
• Tombol SOS + Gas (INPUT_PULLUP)
Firmware & Framework
• PlatformIO + Arduino Framework (C++)
• FreeRTOS — xTaskCreatePinnedToCore (Core 1)
• ArduinoJson v7 — serialisasi JSON
• PubSubClient — MQTT client
• WiFiClientSecure — TLS tanpa verifikasi sertifikat
• WebServer — HTTP sinkron port 80
• Preferences — penyimpanan NVS (WiFi credentials)
Cloud & Infrastruktur
• Firebase Firestore — REST API (documents:commit)
• Google Identity Toolkit — anonymous auth + token
• HiveMQ Cloud — MQTT broker TLS port 8883
• NTP: pool.ntp.org / time.google.com
• mDNS: rorro.local
Mobile & Monitoring
• Flutter app (dikembangkan tim mobile)
• Subscribe MQTT: rollators/<id>/#
• History dari Firestore subcollections
• dashboard.html — control panel lokal
• Tools: imu_tune.py, mqtt_test.py (Python)

## Slide 6
05
Alur Kerja Sistem
Dari sensor ke cloud — deferred-queue pattern
RoRo — Smart Rollator | Firmware ESP32
6 / 10
Sensor / Input
● Potensiometer (ADC)
● Tombol Gas (GPIO 16)
● Tombol SOS (GPIO 4)
● MPU6050 (I2C)
➡
FreeRTOS Task (Core 1 — Realtime)
● TaskMotor (10 ms)
● TaskSafety (20 ms)
● TaskIMU (120 ms)
● portMUX critical section
➡
Queue*() Non-Blocking
● firebaseManagerQueue*()
● mqttManagerQueue*()
● Hanya set flag + cache value
● Tidak blocking
➡
Arduino loop() (Best-Effort)
● wifiManagerLoop()
● firebaseManagerLoop()
● mqttManagerLoop()
● webServerLoop()
➡
Cloud / Output
● Firebase Firestore
● HiveMQ MQTT
● Flutter App
● dashboard.html
⚠ Retry logic: jika Firestore/MQTT gagal, flag pending=true → coba lagi 5 detik kemudian. Tasks tidak pernah blocking karena network.

## Slide 7
06
API & Dashboard Lokal
HTTP port 80 — akses via rorro.local
RoRo — Smart Rollator | Firmware ESP32
7 / 10
HTTP Endpoints
GET
/api/status
Full state: WiFi, gas, SOS, IMU, speeds, uptime
GET
/api/imu/status
Field IMU saja: status, pitch, roll, motionScore
POST
/api/wifi
Simpan SSID+password, restart ke STA mode
POST
/api/provisioning/start
Paksa AP mode, restart untuk re-provisioning
POST
/api/motor/test
Uji motor manual: {left, right, duration_ms}
POST
/api/sos/test
Simulasi SOS: {clear: bool} → queue ke Firebase
MQTT Topics (HiveMQ Retained)
rollators/<id>/gas
{"gas": bool, "deviceMillis": int}
rollators/<id>/sos
{"sos": bool, "deviceMillis": int}
rollators/<id>/imu
{"status": "jalan|diam", "walking": bool, "pitch": float, "motionScore": float}
rollators/<id>/status
{"online": bool} ← Last Will offline
ℹ dashboard.html — standalone HTML, polling /api/status setiap 1 detik. Buka via http://rorro.local atau IP lokal ESP32.

## Slide 8
07
Demo & Screenshot
Demonstrasi sistem berjalan
RoRo — Smart Rollator | Firmware ESP32
8 / 10
[FOTO / SCREENSHOT]
Hardware Rollator
Foto fisik rollator + ESP32 terpasang
[FOTO / SCREENSHOT]
Serial Monitor
Log FreeRTOS: TaskMotor, TaskIMU, TaskSafety
[FOTO / SCREENSHOT]
dashboard.html
Browser membuka http://rorro.local
[FOTO / SCREENSHOT]
Firebase Console
Firestore — dokumen rollator + subcollection history
[FOTO / SCREENSHOT]
Flutter App
Tampilan realtime dari MQTT push
[FOTO / SCREENSHOT]
MQTT Monitor
mqtt_web_monitor.html — topic live feed
Ganti placeholder [FOTO / SCREENSHOT] dengan gambar aktual saat presentasi.

## Slide 9
08
Tim & Kontribusi
Pengembang firmware + mobile
RoRo — Smart Rollator | Firmware ESP32
9 / 10
⚡ Tim Firmware (ESP32)
▶ Arsitektur FreeRTOS
Dual-core task, portMUX locking
▶ Motor Control
BTS7960, PWM, potensiometer, triple-tap latch
▶ IMU Manager
MPU6050, motionScore EMA, state machine
▶ Safety Module
SOS, buzzer, priority 3 task
▶ Firebase Manager
Firestore REST, auth, deferred-queue
▶ MQTT Manager
HiveMQ TLS, retained publish, Last Will
▶ WiFi Manager
AP/STA state machine, mDNS, Preferences
▶ HTTP API
WebServer, dashboard.html, CORS
📱 Tim Mobile (Flutter)
▶ Flutter App
Companion app untuk monitoring rollator
▶ MQTT Subscribe
rollators/<id>/# — realtime state push
▶ Dashboard Realtime
Gas, SOS, IMU walking status, pitch/roll
▶ History & Audit
Firebase Firestore subcollection query
▶ Offline Handling
status.online=false → IMU dianggap offline
▶ Notifikasi SOS
Push notification saat SOS aktif
Nama anggota tim dapat ditambahkan di sini sesuai kebutuhan presentasi.

## Slide 10
09
Kesimpulan & Q&A
RoRo — Smart Rollator | Firmware ESP32
10 / 10
✔ Yang Berhasil Diimplementasikan
✔ Dual-core FreeRTOS: TaskMotor, TaskIMU, TaskSafety
✔ Kendali motor DC via BTS7960 + potentiometer
✔ Deteksi berjalan/diam — MPU6050 + EMA motionScore
✔ Tombol SOS + buzzer state machine
✔ Deferred-queue: tasks tidak blocking networking
✔ Firebase Firestore — storage & history tiap event
✔ MQTT HiveMQ TLS — push realtime ke Flutter
✔ WiFi provisioning AP/STA + mDNS rorro.local
✔ HTTP API lokal + dashboard.html
✔ Tools Python: imu_tune.py, mqtt_test.py
🔧 Pengembangan Selanjutnya
▶ Encoder roda — odometri & feedback loop PID
▶ Monitoring baterai (GPIO 36 ADC)
▶ Fall detection — pitch/roll threshold otomatis
▶ TLS certificate verification (keamanan produksi)
▶ Physical emergency stop button
Terima Kasih
RoRo — Smart Robot Rollator
Ada pertanyaan?
rorro.local • rollators/<id>/#